Using large structures
and
Field API on accelerators

# Introduction
This document describes a possible method for porting the code on devices such as GP-GPUs. This method heavily relies on Field API and Field API based structures.
# Grid-point calculations
## Physics
The interface of physical parametrizations is usually very well defined; for instance the interface of the now famous ACRANEB2 is a list of about 50 NPROMA arrays:
SUBROUTINE ACRANEB2( &
! - INPUT
 & YDERDI,YDRIP,YDML_PHY_MF, &
 & KIDIA,KFDIA,KLON,KTDIA,KLEV,KJN,KSTEP,KNFRRC, &
! - INPUT 2D
 & PAPRS,PAPRSF,PCP,PR,PDELP,PNEB,PQ,PQCO2,PQICE,PQLI,PQO3,PT, &
! - INPUT 1D
 & PALB,PALBDIR,PEMIS,PGELAM,PGEMU,PMU0,PMU0LU,PTS,PDECRD,PCLCT, &
...
TYPE(TERDI) ,INTENT(IN) :: YDERDI
TYPE(MODEL_PHYSICS_MF_TYPE),INTENT(IN) :: YDML_PHY_MF
TYPE(TRIP) ,INTENT(IN) :: YDRIP
...
REAL(KIND=JPRB),INTENT(IN) :: PAPRS(KLON,0:KLEV)
REAL(KIND=JPRB),INTENT(IN) :: PAPRSF(KLON,KLEV)
REAL(KIND=JPRB),INTENT(IN) :: PCP(KLON,KLEV)
...
REAL(KIND=JPRB),INTENT(INOUT) :: PSDUR(KLON)
REAL(KIND=JPRB),INTENT(OUT) :: PFRSO(KLON,0:KLEV)
...

From the subroutine interface it is therefore quite easy to identify the data which needs to be synchronized on the device. We also notice that some of the constant structures we pass as arguments may contain some dynamically allocated data that would require special care to be used on the device; we describe a method for deep copying these structures on the device farther in this document.
## Grid-point dynamics
The situation is quite different for grid-point dynamics; for instance cpg_gp.F90 has now the following interface :
SUBROUTINE CPG_GP(YDGEOMETRY, YDCPG_BNDS, YDCPG_OPTS, YDCPG_TND, &
& YDCPG_MISC, YDCPG_GPAR, YDCPG_DYN0, YDCPG_DYN9, YDMF_PHYS_SURF, &
& YDVARS, YDMODEL, YDCPG_SL2, YDDDH)
TYPE(GEOMETRY) ,INTENT(IN) :: YDGEOMETRY
TYPE(CPG_BNDS_TYPE) ,INTENT(IN) :: YDCPG_BNDS
TYPE(CPG_OPTS_TYPE) ,INTENT(IN) :: YDCPG_OPTS
TYPE(CPG_TND_TYPE) ,INTENT(INOUT) :: YDCPG_TND ~8
TYPE(CPG_MISC_TYPE) ,INTENT(INOUT) :: YDCPG_MISC ~15
TYPE(CPG_GPAR_TYPE) ,INTENT(INOUT) :: YDCPG_GPAR ~19
TYPE(CPG_DYN_TYPE) ,INTENT(INOUT) :: YDCPG_DYN0 ~45
TYPE(CPG_DYN_TYPE) ,INTENT(INOUT) :: YDCPG_DYN9 ~45
TYPE(MF_PHYS_SURF_TYPE) ,INTENT(INOUT) :: YDMF_PHYS_SURF ~200
TYPE(FIELD_VARIABLES) ,INTENT(INOUT) :: YDVARS ~500
TYPE(MODEL) ,INTENT(IN) :: YDMODEL
TYPE(CPG_SL2_TYPE) ,INTENT(INOUT) :: YDCPG_SL2
TYPE(TYP_DDH) ,INTENT(INOUT) :: YDDDH

We see here that plenty of arguments are structures based on Field API objects (those with a green highlight). We have added the approximate number of Field API objects contained in these structures.
The code spanned by cpg_gp.F90 is quite large and these structures are passed and used extensively in most of non terminal routines. We have highlighted in red those where iterations over members of YDVARS are necessary.

It is therefore impossible to make a proper guess of which members of cpg_gp.F90 arguments are required to be synchronized on the device, just by studying the interface of cpg_gp.F90. Furthermore, we consider that making these structures accessible on the device would make things much easier for porting the code.
We describe a possible method for tackling these issues farther in this document.
# A small test case: cpg_dia_flu.F90
Below is the list of arguments of cpg_dia_flu.F90; most of them are structures wrapping Field API data:
TYPE(CPG_BNDS_TYPE) ,INTENT(IN) :: YDCPG_BNDS
TYPE(CPG_OPTS_TYPE) ,INTENT(IN) :: YDCPG_OPTS
TYPE(CPG_MISC_TYPE) ,INTENT(IN) :: YDCPG_MIS
TYPE(MF_PHYS_OUT_TYPE) ,INTENT(IN) :: YDMF_PHYS_OUT
TYPE(CPG_DYN_TYPE) ,INTENT(IN) :: YDCPG_DYN0
TYPE(MF_PHYS_SURF_TYPE) ,INTENT(IN) :: YDMF_PHYS_SURF
TYPE(FIELD_VARIABLES) ,INTENT(IN) :: YDVARS
TYPE(TCFU) ,INTENT(INOUT):: YDCFU
TYPE(TXFU) ,INTENT(INOUT):: YDXFU
TYPE(MODEL) ,INTENT(IN) :: YDMODEL

Numbers are the number of lines of each routine. Routines without such numbers are CONTAINed routines, meant to be inlined.
This small test case contains the problem we need to solve; although it is small and does very little processing (it just accumulates or records quantities computed in ARPEGE/AROME physics, with possibly some light computations), it uses deeply nested structures, some of which are based on Field API. We shall rely on this test case to illustrate the different methods we propose.
The code is available on ecgate :
XXXXXXXXXXXXXXXXXXX
And on github :
 https://github.com/pmarguinaud/cpg_dia_flu
# Large constant structures: YDMODEL, YDGEOMETRY
We have now a long experience of serializing/de-serializing these structures, for creating stand-alone test cases. We also generate code for creating and initializing these large structures on the device.
We proceed by inspecting the type definitions with a script and generating code.
The result for YDMODEL can be seen in support/util_model_mod.F90. Four routines are generated, and aggregated to GENERIC interfaces:
INTERFACE SAVE
MODULE PROCEDURE SAVE_MODEL
END INTERFACE

INTERFACE LOAD
MODULE PROCEDURE LOAD_MODEL
END INTERFACE

INTERFACE COPY
MODULE PROCEDURE COPY_MODEL
END INTERFACE

INTERFACE WIPE
MODULE PROCEDURE WIPE_MODEL
END INTERFACE

SUBROUTINE SAVE_MODEL (KLUN, YD) !<-- Save MODEL to unit KLUN
INTEGER, INTENT (IN) :: KLUN
TYPE (MODEL), INTENT (IN), TARGET :: YD
...
SUBROUTINE LOAD_MODEL (KLUN, YD) !<-- Load MODEL from unit KLUN
INTEGER, INTENT (IN) :: KLUN
TYPE (MODEL), INTENT (OUT), TARGET :: YD
...
SUBROUTINE COPY_MODEL (YD, LDCREATED) !<-- Duplicate MODEL on the device
TYPE (MODEL), INTENT (IN), TARGET :: YD
LOGICAL, OPTIONAL, INTENT (IN) :: LDCREATED
...
SUBROUTINE WIPE_MODEL (YD, LDDELETED) !<-- Delete MODEL on the device
TYPE (MODEL), INTENT (IN), TARGET :: YD
LOGICAL, OPTIONAL, INTENT (IN) :: LDDELETED
...

MODEL utility routines (SAVE, LOAD, COPY, WIPE) use other utility routines (derived from MODEL type members), which in turn may use other routines, etc.
POINTER and ALLOCATABLE members have to be handled specifically using OpenACC directives; for instance:
SUBROUTINE COPY_MODEL (YD, LDCREATED)
TYPE (MODEL), INTENT (IN), TARGET :: YD
...
LYRCST = ASSOCIATED (YD%YRCST)
IF (LYRCST) THEN
  !$acc enter data create (YD%YRCST)
  !$acc update device (YD%YRCST)
  CALL COPY (YD%YRCST, LDCREATED=.TRUE.)
  !$acc enter data attach (YD%YRCST)
ENDIF

Having MODEL and GEOMETRY objects permanently available on the device looks therefore very feasible, assuming their non-constant parts have been clearly identified.
Defining utility methods in external modules has its limits: PRIVATE members of derived types cannot be accessed for saving/loading/copying the structures. The best solution would be to define these utility functions as methods in the module defining the derived type; we have a prototype of such a pre-processor for modifying derived types definitions before compilation; for instance:
TYPE, PUBLIC :: MODEL
...
CONTAINS
  PROCEDURE :: SAVE => SAVE_MODEL
  PROCEDURE :: LOAD => LOAD_MODEL
  PROCEDURE :: COPY => COPY_MODEL
  PROCEDURE :: WIPE => WIPE_MODEL
END TYPE
...
CONTAINS
SUBROUTINE SAVE_MODEL (YD, KLUN)
IMPLICIT NONE
CLASS (MODEL), INTENT (IN), TARGET :: YD
...

Such an approach also has implications and has to be discussed; for instance:
- SEQUENCE is forbidden
- BIND (C) is forbidden
# Field API based structures
## Copying structures to the accelerator
Field API based structures can also be saved, loaded back and copied to the device. The following points, however, require special attention:
- Field API objects utility methods shall not be generated automatically, but must be written by the programmer (see support/util_field_mod.fypp).
- The members (pointers) implementing a single block view on a Field API object shall be ignored by utility methods.
- Loading a Field API object from disk always selects the FIELD_OWNER class, even if the saved field belonged to the FIELD_WRAPPER class.
- Copying a Field API object to the device is different from syncing its data: the former copies the object without its field data to the device, while the latter creates a copy of the field data on the device.
We can therefore push YDVARS and other Field API based structures on the device, using the very same method we use for YDGEOMETRY and YDMODEL, the difference being that the code for handling Field API members is not generated automatically and that the data managed by Field API is not copied, but requires a call to the SYNC_DEVICE method to be available on the device.
## Syncing Field API backed data
We made all existing Field API classes inherit a common abstract class:
TYPE, ABSTRACT :: FIELD_BASIC
  LOGICAL :: THREAD_BUFFER = .FALSE.
  INTEGER(KIND=JPIM) :: ISTATUS = 0
...
  LOGICAL :: LOBJECT_COPIED = .FALSE. ! Object copied on device or not
CONTAINS
  PROCEDURE (SYNC), DEFERRED :: SYNC_HOST_RDWR
  PROCEDURE (SYNC), DEFERRED :: SYNC_HOST_RDONLY
  PROCEDURE (SYNC), DEFERRED :: SYNC_DEVICE_RDWR
  PROCEDURE (SYNC), DEFERRED :: SYNC_DEVICE_RDONLY
END TYPE FIELD_BASIC

ABSTRACT INTERFACE
  SUBROUTINE SYNC (SELF)
    IMPORT FIELD_BASIC
    CLASS(FIELD_BASIC), INTENT (INOUT) :: SELF
  END SUBROUTINE
END INTERFACE

TYPE, ABSTRACT, EXTENDS (FIELD_BASIC) :: FIELD_2D
...

Therefore, all pointers on any Field API object can be cast to FIELD_BASIC, passed along to some other routines, and synchronization methods can be called on the object. Up-casting to a common base class will make it possible to generate synchronization methods, as we shall see later.
Let us now look at a simple but typical parallel loop of our test case:
DO JLEV=0,YDCPG_OPTS%KFLEVG
  ZSTRCU(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRCU(KIDIA:KFDIA,JLEV)
  ZSTRCV(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRCV(KIDIA:KFDIA,JLEV)
...
ENDDO

Such a piece of code can easily be analysed and transformed to:
IF (ASSOCIATED (YDMF_PHYS_OUT%F_STRCU)) CALL YDMF_PHYS_OUT%F_STRCU%SYNC_DEVICE_RDONLY
IF (ASSOCIATED (YDMF_PHYS_OUT%F_STRCV)) CALL YDMF_PHYS_OUT%F_STRCV%SYNC_DEVICE_RDONLY

All assignment statements can therefore be transformed so that all Field API objects be synced RDONLY when they appear in the right hand side or synced RDWR when they appear in the left hand side.
A call to a routine is dealt as in this example; the following sample code:
CALL MEANWIND_XFU (YDCPG_OPTS, YDCPG_BNDS, NMEANSTEPS, YDXFU%UCLS, YDXFU%VCLS,&
        & PXUCLS, PXVCLS, YDXFU%RMWINDCALC, ZUMEAN, ZVMEAN)

becomes:
YLFLDPTR0 => YDXFU%F_UCLS ! Upcasting
YLFLDPTR1 => YDXFU%F_VCLS ! Upcasting
YLFLDPTR2 => YDXFU%F_RMWINDCALC ! Upcasting
CALL MEANWIND_XFU_SYNC_HOST (YDCPG_OPTS, YDCPG_BNDS, NMEANSTEPS, &
 & YLFLDPTR0, YLFLDPTR1, PXUCLS, PXVCLS, YLFLDPTR2, ZUMEAN, ZVMEAN)

Up-casting allows us to pass Field API objects of any dimension to synchronization routines: in the original NPROMA blocked code, the actual argument could be an array of dimension 2 or a slice of an array of dimension 3. It is therefore important to work with objects whose class is independent of the dimension.
It looks therefore possible to generate automatically routines whose sole purpose would be the synchronization of data required for executing a routine on the device (or on the host). These routines can be derived from the original code, keeping all the original logic (IF/THEN/ELSE constructs), and may in turn call other routines achieving the same purpose.
Simplifying these routines is possible, but not detailed here. Making the transfers asynchronous looks also possible but has not been tried yet.
The reader is invited to look at the following routines:
- cpg_dia_flu.F90
- cpg_dia_flu_sync_device.F90

In the diagram above, we could avoid to generate synchronization code for routines which do not take any Field API backed structures as arguments (such as meanwind_xfu.F90 and dprecips_xfu.F90); instead we could operate synchronization based on the INTENT of their arguments.
## Using Field API objects in the calculations
The following code (from cpg_dia_flu.F90):
ZUCLS(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA)=ZUCLS(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA) &
      & /YDVARS%GEOMETRY%GM%T0(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA)

ZVCLS(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA)=ZVCLS(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA) &
      & /YDVARS%GEOMETRY%GM%T0(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA)

Can be transformed into a OpenMP parallel section;
!$OMP PARALLEL DO &
!$OMP&FIRSTPRIVATE (YDCPG_BNDS, YL_ZUCLS, YL_ZVCLS, YDVARS, ...) &
!$OMP&PRIVATE (IBL, JLEV)

DO IBL = 1, YDCPG_OPTS%KGPBLKS
  CALL YDCPG_BNDS%UPDATE_VIEW (BLOCK_INDEX=IBL)
  CALL YL_ZUCLS%UPDATE_VIEW (BLOCK_INDEX=IBL)
  CALL YL_ZVCLS%UPDATE_VIEW (BLOCK_INDEX=IBL)
  CALL YDVARS%UPDATE_VIEW (BLOCK_INDEX=IBL)
...
  YL_ZUCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)= &
& YL_ZUCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL) &
& /YDVARS%GEOMETRY%GM%FT0%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)

  YL_ZVCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)= &
& YL_ZVCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL) &
& /YDVARS%GEOMETRY%GM%FT0%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)

Or to an OpenMP parallel section, accessing directly Field API data (this has the obvious advantage of not calling the expensive UPDATE_VIEW methods on Field API structures):

!$OMP PARALLEL DO &
!$OMP&FIRSTPRIVATE (YDCPG_BNDS) &
!$OMP&PRIVATE (IBL, JLEV)

DO IBL = 1, YDCPG_OPTS%KGPBLKS
  CALL YDCPG_BNDS%UPDATE_VIEW (BLOCK_INDEX=IBL)

  YL_ZUCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)= &
& YL_ZUCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL) &
& /YDVARS%GEOMETRY%GM%FT0%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)

  YL_ZVCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)= &
& YL_ZVCLS%F_P%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL) &
& /YDVARS%GEOMETRY%GM%FT0%PTR(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,YDCPG_BNDS%KBL)

Note that the temporaries (ZUCLS, ZVCLS) have been wrapped into ARRAY_2D or ARRAY_3D objects (based on Field API). See cpg_dia_flu.F90 and cpg_dia_flu_parallel.F90 for more details.
## Using structures on the accelerator
This is now possible, assuming that
large structures (YDMODEL, YDVARS, etc.) have been created on the device. We do that in the main program (wrap_cpg_dia_flux.F90):
CALL COPY (YLMODEL)
CALL COPY (YLVARS)
CALL COPY (YLCPG_OPTS)
CALL COPY (YLCPG_MISC)
CALL COPY (YLCPG_DYN0)
CALL COPY (YLXFU)
CALL COPY (YLCFU)
CALL COPY (YLMF_PHYS_OUT)
CALL COPY (YLMF_PHYS_SURF)

temporaries are copied to the device when a parallel routine (such as cpg_dia_flu_parallel.F90) is entered:
CALL YL_ZDPRECIPS%INIT (UBOUNDS=[YDCPG_OPTS%KLON,YDMODEL%YRML_PHY_MF%YRPHY%YRDPRECIPS%NDTPREC,YDCPG_OPTS%KGPBLKS], PERSISTENT=.TRUE.)
CALL COPY (YL_ZDPRECIPS)
CALL YL_ZDPRECIPS2%INIT (UBOUNDS=[YDCPG_OPTS%KLON,YDMODEL%YRML_PHY_MF%YRPHY%YRDPRECIPS%NDTPREC2,YDCPG_OPTS%KGPBLKS], PERSISTENT=.TRUE.)
CALL COPY (YL_ZDPRECIPS2)

Deleting temporaries from the device is mandatory at the end of the scope of the routine, as well as deleting their data:
CALL WIPE (YL_ZNVCLS) ! Delete structure on device
CALL YL_ZNVCLS%FINAL ! Delete field data (DEVPTR & PTR if not NULL)
CALL WIPE (YL_ZVCLS)
CALL YL_ZVCLS%FINAL

Eventually, note that:
- Passing large data structures to OpenACC kernels disables checks made by OpenACC on field data itself; a first level check is performed on these structures, without following pointers members that may be defined in the structures themselves.
- COPY and WIPE methods could be hidden in constructor and destructor methods.
- Allocation of temporaries could be deferred until first synchronization. A destruction plan could also be generated, in order to deallocate them when they are used for the last time.
# Running single column kernels
We have enabled a single OpenACC kernel on a NVIDIA V100. This is the following piece of code, processing a single block, taken from cpg_dia_flu.F90:
IF (YDMODEL%YRML_PHY_MF%YRPHY%LDPRECIPS) THEN
  ZDPRECIPS(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,:)=&
  & YDMF_PHYS_SURF%GSD_XP%PPRECIP(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,:)
ENDIF

IF (YDMODEL%YRML_PHY_MF%YRPHY%LDPRECIPS2) THEN
  ZDPRECIPS2(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,:)= &
 & YDMF_PHYS_SURF%GSD_XP2%PPRECIP2(YDCPG_BNDS%KIDIA:YDCPG_BNDS%KFDIA,:)
ENDIF

CALL CPXFU(YDXFU, YDMODEL%YRML_PHY_MF%YRPHY%YRDPRECIPS, YDCPG_OPTS, &
& YDCPG_BNDS, YDMF_PHYS_OUT, YDCPG_MISC, ZSTRCU, ZSTRCV, ZSTRDU, ZSTRDV, &
& ZSTRTU, ZSTRTV, ZUCLS, ZVCLS, ZNUCLS, ZNVCLS, ZUGST, ZVGST, ZDPRECIPS, &
& ZDPRECIPS2)

This code can be transformed into:
! Field API data synchronization

CALL CPG_DIA_FLU_PARALLEL_1_SYNC_DEVICE (YDCPG_BNDS, YDCPG_OPTS, YDCPG_MISC, YDMF_PHYS_OUT, &
& YDMF_PHYS_SURF, YDXFU, YDMODEL, YL_ZDPRECIPS, YL_ZDPRECIPS2, YL_ZNUCLS, YL_ZNVCLS, YL_ZSTRCU, &
& YL_ZSTRCV, YL_ZSTRDU, YL_ZSTRDV, YL_ZSTRTU, YL_ZSTRTV, YL_ZUCLS, YL_ZUGST, YL_ZVCLS, YL_ZVGST)

! Loop on blocks

!$ACC PARALLEL LOOP GANG &
!$ACC&FIRSTPRIVATE (YDCPG_BNDS, YDSTACK) &
!$ACC&PRIVATE (IBL)

DO IBL = 1, YDCPG_OPTS%KGPBLKS
  YDCPG_BNDS%KBL = IBL
  YDCPG_BNDS%KSTGLO = 1 + (IBL - 1) * YDCPG_BNDS%KLON
  YDCPG_BNDS%KFDIA = MIN (YDCPG_BNDS%KLON, YDCPG_BNDS%KGPCOMP - YDCPG_BNDS%KSTGLO + 1)
  ! Per block stack setup
  YDSTACK%L = LOC (YDSTACK%F_P%DEVPTR (1,IBL))
  YDSTACK%U = YDSTACK%L + KIND (YDSTACK%F_P%DEVPTR) * SIZE (YDSTACK%F_P%DEVPTR (:,IBL))

!$ACC LOOP VECTOR &
!$ACC&PRIVATE (JLON, YLCPG_BNDS)

  ! Loop on block elements
  DO JLON = YDCPG_BNDS%KIDIA, YDCPG_BNDS%KFDIA
    ! Select single column
    YLCPG_BNDS = YDCPG_BNDS
    YLCPG_BNDS%KIDIA = JLON
    YLCPG_BNDS%KFDIA = JLON

    IF (YDMODEL%YRML_PHY_MF%YRPHY%LDPRECIPS) THEN
      YL_ZDPRECIPS%F_P%DEVPTR(JLON,:,YLCPG_BNDS%KBL) = &
       & YDMF_PHYS_SURF%GSD_XP%F_PRECIP%DEVPTR(JLON,:,YLCPG_BNDS%KBL)
    ENDIF

    IF (YDMODEL%YRML_PHY_MF%YRPHY%LDPRECIPS2) THEN
      YL_ZDPRECIPS2%F_P%DEVPTR(JLON,:,YLCPG_BNDS%KBL) = &
        & YDMF_PHYS_SURF%GSD_XP2%F_PRECIP2%DEVPTR(JLON,:,YLCPG_BNDS%KBL)
    ENDIF

    CALL CPXFU_SINGLE_COLUMN_FIELD_API_DEVICE(YDXFU, YDMODEL%YRML_PHY_MF%YRPHY%YRDPRECIPS, &
    & YDCPG_OPTS, YLCPG_BNDS, YDMF_PHYS_OUT, YDCPG_MISC, YL_ZSTRCU%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL),&
    & YL_ZSTRCV%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YL_ZSTRDU%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), &
    & YL_ZSTRDV%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YL_ZSTRTU%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), &
    & YL_ZSTRTV%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YL_ZUCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), &
    & YL_ZVCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), YL_ZNUCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), &
    & YL_ZNVCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), YL_ZUGST%F_P%DEVPTR(:,YLCPG_BNDS%KBL), &
    & YL_ZVGST%F_P%DEVPTR(:,YLCPG_BNDS%KBL), YL_ZDPRECIPS%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), &
    & YL_ZDPRECIPS2%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YDSTACK)

  ENDDO
ENDDO

We use a STACK object so that the kernel be able to allocate temporary memory, and we directly use the DEVPTR member of Field API objects. All structures involved in the calculations have been copied to the device, and field data has been synchronized on the device before the kernel starts.
The routine cpxfu_single_column_field_api_device.F90 has been generated from cpxfu.F90; its code is available here : compile.gpu_nvhpc/cpxfu_single_column_field_api_device.F90.
Eventually, note that the code described above does not currently work with PGI (though it should, and a bug has been filed); for now, we need to move the vector loop inside a vector routine. This routine is visible here : compile.gpu_nvhpc/cpg_dia_flu_parallel_1.F90.
# Directives
## GENERATE directives
Code generation is based on directives; for instance :
SUBROUTINE CPG_DIA_FLU (YDCPG_BNDS, YDCPG_OPTS, YDCPG_MISC, YDMF_PHYS_OUT, YDCPG_DYN0, &
& YDMF_PHYS_SURF, YDVARS, YDCFU, YDXFU, YDMODEL)

!=GENERATE= TARGET=SyncDevice
!=GENERATE= TARGET=SyncHost/Parallel/SingleColumnFieldAPIHost/FieldAPIHost

...

!=PARALLEL TARGET=HOST

!* 2.2 DIVIDE SOME QUANTITIES LINKED TO (U,V) BY THE MAPPING FACTOR.

! * ZSTR.. arrays are used for CFU, XFU and in CUMCPL.
IF (LLCALL_CPCFU.OR.LLCALL_CPXFU.OR.LLCALL_CUMCPLDM) THEN
  DO JLEV=0,YDCPG_OPTS%KFLEVG
    ZSTRCU(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRCU(KIDIA:KFDIA,JLEV)
    ZSTRCV(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRCV(KIDIA:KFDIA,JLEV)
    ZSTRDU(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRDU(KIDIA:KFDIA,JLEV)
    ZSTRDV(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRDV(KIDIA:KFDIA,JLEV)
    ZSTRTU(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRTU(KIDIA:KFDIA,JLEV)
    ZSTRTV(KIDIA:KFDIA,JLEV)=YDMF_PHYS_OUT%STRTV(KIDIA:KFDIA,JLEV)
  ENDDO
ENDIF

!=END PARALLEL

The GENERATE directives at the top of the routine will trigger several transformations of the routine, each of these transformations creating a single routine:
	Routine name	Purpose
SyncDevice	cpg_dia_flu_sync_device.F90	Synchronize all field data for running cpg_dia_flu.F90 on the device
SyncHost	cpg_dia_flu_sync_host.F90	Synchronize all field data for running cpg_dia_flu.F90 on the host
Parallel	cpg_dia_flu_parallel.F90	Process a list of blocks with using several parallel sections
SingleColumnFieldAPIHost	cpg_dia_flu_single_column_field_api_host.F90	Calculations using directly Field API objects on the host; this routine will process a single column
FieldAPIHost	cpg_dia_flu_field_api_host.F90	Calculations using directly Field API objects on the host

## PARALLEL directives
PARALLEL directives are use by the Parallel transformation. Each of these will create a parallel loop on NPROMA blocks, either with OpenMP or OpenACC. For instance, cpg_dia_flu.F90 contains two of these PARALLEL directives:
!=PARALLEL TARGET=HOST

! Generate code with OpenMP on the CPU (default)

...

!=PARALLEL TARGET=DEVICE,VECTOR=SINGLECOLUMN,DIRECTIVE=OPENACC

! Generate code for a parallel section with OpenACC directives on the GPU,
! using the single column method for distributing columns on the device

Each of these parallel section will also trigger the creation of synchronization code; that is, in the case of cpg_dia_flu.F90 :
- compile.gpu_nvhpc/cpg_dia_flu_parallel_0_sync_host.F90 (first PARALLEL directive, targeting the host)
- compile.gpu_nvhpc/cpg_dia_flu_parallel_1_sync_device.F90 (second PARALLEL directive, with TARGET=DEVICE)
## The big picture
The parallel version (processing a list of NPROMA blocks using several kernels) of cpg_dia_flu.F90 therefore looks like the following:

We observe on this diagram that a lot of synchronization code have been generated and attached to the parallel routines (cpg_dia_flu_parallel.F90 and cpcfu_parallel.F90). The structure of this synchronization code reflects the original organization of the code, but terminal routines not relying on Field API based structures could be removed, assuming we could exploit the INTENTs of their arguments.
# Validation
Only YDXFU and YDCFU members are affected by cpg_dia_flu.F90. We measure tiny differences when we compare results obtained on NVIDIA V100 with a reference prepared on AMD Rome using the Intel compiler:
$ ./compile.gpu_nvhpc/wrap_cpg_dia_flux.x --case t0031 –diff --parallel
      TCFU%FCCQL 31 8 1 0.5422E-09 0.5422E-09 -0.1034E-24
      TCFU%FCCQL 5 6 2 0.1343E-16 0.1343E-16 0.1541E-32
      TCFU%FCCQL 32 6 2 0.2652E-17 0.2652E-17 0.3852E-33
      TCFU%FCCQL 5 7 2 0.2732E-10 0.2732E-10 -0.3231E-26
...

There are, however, no differences with a reference prepared with the PGI compiler on AMD Rome.
# Possible caveat
Field API objects are directly dereferenced in call statements, when transforming single block code into parallel code; for instance:

  CALL CPXFU(YDXFU, YDMODEL%YRML_PHY_MF%YRPHY%YRDPRECIPS, YDCPG_OPTS, YDCPG_BNDS, YDMF_PHYS_OUT, &
  & YDCPG_MISC, ZSTRCU, ZSTRCV, ZSTRDU, ZSTRDV, ZSTRTU, ZSTRTV, ZUCLS, ZVCLS, ZNUCLS, ZNVCLS, &
  & ZUGST, ZVGST, ZDPRECIPS, ZDPRECIPS2)

becomes:
    CALL CPXFU_SINGLE_COLUMN_FIELD_API_DEVICE(YDXFU, YDMODEL%YRML_PHY_MF%YRPHY%YRDPRECIPS, &
    & YDCPG_OPTS, YLCPG_BNDS, YDMF_PHYS_OUT, YDCPG_MISC, YL_ZSTRCU%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL),&
    & YL_ZSTRCV%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YL_ZSTRDU%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), &
    & YL_ZSTRDV%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YL_ZSTRTU%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), &
    & YL_ZSTRTV%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YL_ZUCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), &
    & YL_ZVCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), YL_ZNUCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), &
    & YL_ZNVCLS%F_P%DEVPTR(:,YLCPG_BNDS%KBL), YL_ZUGST%F_P%DEVPTR(:,YLCPG_BNDS%KBL), &
    & YL_ZVGST%F_P%DEVPTR(:,YLCPG_BNDS%KBL), YL_ZDPRECIPS%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), &
    & YL_ZDPRECIPS2%F_P%DEVPTR(:,:,YLCPG_BNDS%KBL), YDSTACK)

This means that when the routine is invoked, all Field API members have to be allocated; and it is important to emphasize that some of these members are allocated only when some particular options are active (eg the non-hydrostatic settings of the model enable the allocation of extra fields).

In FORTRAN, it is possible to have routines with optional arguments; what is less known is the following (from ISO/IEC 1539-1/2010):

12.5.2.12 Argument presence and restrictions on arguments not present
A dummy argument or an entity that is host associated with a dummy argument is not present if the dummy argument
- does not correspond to an actual argument,
- corresponds to an actual argument that is not present, or
- does not have the ALLOCATABLE or POINTER attribute, and corresponds to an actual argument that
  - has the ALLOCATABLE attribute and is not allocated, or
  - has the POINTER attribute and is disassociated.

This is best illustrated by the following piece of code:
SUBROUTINE SUB (PX, PY)
REAL, INTENT (IN) :: PX (:)
REAL, INTENT (IN), OPTIONAL :: PY (:)
...
END SUBROUTINE

...

ZY => NULL ()
CALL SUB (ZX, ZY) ! PRESENT (PY) is .FALSE. in SUB

It is clear that exploiting this feature of FORTRAN would not work with the full dereferencing of Field API objects. Hopefully, we do not use (too much) this feature; instead, routines with optional arguments are called from contexts where their optional arguments are valid.
# Conclusion
From studying this small test case it appears that:
- using large constant structures on the device is possible, assuming that these structures are organized properly (no SEQUENCE or BIND(C), no cyclic graph, possibly some annotations/directives to exclude some members, etc.)
- using large structures based on Field API on the device is also possible and should/could be considered as an opportunity (if not a sine qua non condition) for some of the routines of cpg.F90.
- a flexible framework based on directives for porting the code can be designed.
- the methods described in this document are, in principle, applicable to any routine performing 1D grid point calculations in ARPEGE/IFS, assuming the code is “well written” and relies on Field API.